## Slide 1: On-the-fly Pvs
By Christopher Slominski – June 2023

## Slide 2: What are OTF Pvs?
EPICS process variables created and destroyed within the scope of an application.
  Or even within some internal scope of an application (function, …).
Network variables only.
  Just uses EPICS Channel Access as a means to have global variables.
  No IOC apps.
  Independent variables; no CAPFAST style control relations.

## Slide 3: Why Otf pvs?
Match the lifespan of the PVs to the app that manages them.
  App exiting means PVs become unresolved.
Temporary short term PVs.
  Application test suites.
  Application “what if?” Scenarios.
  OTF EDM screen replay of Mya history.

## Slide 4: Match app lifespan
Don’t want a PV available in the control system to be misconstrued as value valid.
Unresolved PVs are more alerting than a not-blinking watchdog PV on an EDM screen.
Mya Plot showing value over a timespan is misleading when value really is unknown.
Mya Statistics over a span can be severely biased by a last known value persisting past its known value.
Decommissioning an app means automatic decommissioning of associated PVs.

## Slide 5: Channel Access Application Test suites
Matching test results against previously vetted values require repeatable PV values.
Unique OTF PV names vs private duplicated PV names.
The ecalib test suite example.

## Slide 6: “What if” scenarios
Use private duplicated PV names to setup desired scenarios for apps.
Adam’s LEM study.
  Find Energy reach.
  Find which factor is the most limiting.

## Slide 7: OTF screen replay
Show Mya historical values on existing OTF screens.
Study recent critical events via EDM.
Operator training.
This technique has a long way to go to be ready for production.
  Not every field of every record is being archived.
  Must match correct record types when making OTF PVs.
  See notes.docx
Show simple demonstration.

## Slide 8: C++ Library class (ecalib)
The ECA::SoftIoc class manages the lifetime of a EPICS Soft IOC.
Could be “swigged” for use by scripting languages.
Show documentation.
Show simple example.

## Slide 9: Production example (BEM)
Runs on opsbat9; which is Soft IOC enabled for OPS Name Server.
Pertinent apps sharing PVs
  BEM daemon
  BEM EDM screen
  Energy Locks daemon
  Energy Locks GUI
  Mya
Show in action.

## Slide 10: Controlling PV exposure
Developers using this technique must think about this.
Clients use EPICS_CA_ADDRESS_LIST from UNIX environment.
Name Servers use configured list of domains and hosts.
  How can I keep OTF PVs from showing up in the Name Server when I don’t want them to?