## Slide 1: FT Moller shield design
The Moller Shield for operation with the Forward Tagger was designed studying the transverse size of the beam halo as a function of the distance from the target
Assumptions:
The shield is shaped as a truncated cone, pointing to to the CLAS12 center
The shield is made of a single material, i.e. tungsten
To maximize the FT acceptance, the cone angle should be as low as possible compatibly with the CLAS12 and FT operation at L=1035 cm-2s-1
The z coordinate of cone entrance face should be chosen to minimize background on the FT and CLAS12

## Slide 2: Beam Halo Size
The transverse size of the beam halo (“moller sausage”) was studied in GEMC, using “flux” detectors to sample the beam spot at different positions in z
GEMC configuration:
Solenoid field at nominal (max) intensity
Air in the Hall
“flux” detectors

## Slide 3: Beam Halo
The moller spot is always larger than the size of a 2 deg cone
A 2.5 deg. cone can contain most of the background
Optimal z of the cone entrance is at 75 cm from the target
z=50 cm
z=75 cm
z=100 cm
All particles
Electrons
Moller electrons
Moller electrons E>200 MeV
Photons
Others
The lines indicate the size of a cone with 2 deg. and 2.5 deg. aperture

## Slide 4: Final Configuration
DC occupancy
R1 background origin

## Slide 5: Configurations Studied (So far)
No FT Original Design, corrected. It’s the “Baseline”.
No FT. Lead in place of FT.
FT Not Operational, as shielding. Lead in front of FT Cone
FT Configuration
FT Cone

## Slide 6: New (Corrected) Baseline
Realistic (Straight) beamline pipe
Mount to torus
Downstream shield in installed position
Nose to downstream shield
Tungsten Shield around beampipe inside torus
Torus Warm Bore
Torus Warm Bore Shield
Torus Cold Hub

## Slide 7: New (Corrected) Baseline
Realistic (Straight) beamline pipe
Mount to torus
Downstream shield in installed position
Nose to downstream shield
Tungsten Shield around beampipe inside torus
Torus Warm Bore
Torus Warm Bore Shield
Torus Cold Hub

## Slide 8: New (Corrected) Baseline
Realistic (Straight) beamline pipe
Mount to torus
Downstream shield in installed position
Nose to downstream shield
Tungsten Shield around beampipe inside torus
Torus Warm Bore
Torus Warm Bore Shield
Torus Cold Hub

## Slide 9: New (Corrected) Baseline
Realistic (Straight) beamline pipe
Mount to torus
Downstream shield in installed position
Nose to downstream shield
Tungsten Shield around beampipe inside torus
Torus Warm Bore
Torus Warm Bore Shield
Torus Cold Hub

## Slide 10: New (Corrected) Baseline
Realistic (Straight) beamline pipe
Mount to torus
Downstream shield in installed position
Nose to downstream shield
Tungsten Shield around Al beampipe inside torus, 2cm, 12 cm OD
Torus Warm Bore
Torus Warm Bore Shield
Torus Cold Hub
Also: torus vacuum jacket, plates, coils box and coils

## Slide 11: New (Corrected) Baseline
90 mm at z=1390mm: 3.7o
30mm at z=420mm: 4o
Torus Start: z=2753mm
Mount Start: z=2270mm

## Slide 12: New (Corrected) Baseline
R1 Background Source
R3 Background Source

## Slide 13: FT Cone. No FT. Lead in place of FT.
FT Cone moved upstream
Lead Shielding instead of FT
Same Mount
Same configuration downstream

## Slide 14: FT Cone. No FT. Lead in place of FT.
R=120 at z=1444mm: 4.75o
Torus Start: z=2753mm
Mount Start: z=2270mm
SST Support inside tube and cone

## Slide 15: FT Cone. No FT. Lead in place of FT.
R1 Background Source
R3 Background Source

## Slide 16: FT not operational, as shielding.
FT Cone moved upstream
Lead Shielding upstream of FT
Same Mount
Same configuration downstream

## Slide 17: FT not operational, as shielding.
Torus Start: z=2753.8mm
Mount Start: z=2269.6mm
R=120 at z=1444mm: 4.75o

## Slide 18: FT not operational, as shielding.
R1 Background Source
R3 Background Source

## Slide 19: FT Configuration
FT Cone in its nominal position
Same Mount
Same configuration downstream

## Slide 20: FT Configuration
Torus Start: z=2753mm
Mount Start: z=2270mm
R=76mm at z=1760mm: 2.5o

## Slide 21: FT Configuration
R1 Background Source
R3 Background Source