## Slide 1
2018 Requested experimental set-up
Electron energies = 7.5 GeV and 6.5 GeV in 2018
Torus current = + 100% negative outbending
Solenoid Current = - 100 %
Forward Tracker = No
Forward Tagger = YES
Luminosity as high as possible, limited by acquisition rate = 12-14 kHz

## Slide 2
Run Group K Triggers Configuration E=7.5 GeV
Trigger Number | Physics Definition | Detectors Conditions | Thresholds | prescale
0 | 1 electron in CLAS All sectors – with DC | (DC x HTTC x ECAL x PCAL) or (DC x HTTC x PCAL) | (PCAL+ECAL)> 300 MeV PCAL>60 MeV ECAL>10 MeV or PCAL> 300 MeV | 1
1-6 | 1 electron in CLAS Fixed Sector – with DC | (DC x HTTC x ECAL x PCAL) or (DC x HTTC x PCAL) | (PCAL+ECAL)> 300 MeV PCAL>60 MeV ECAL>10 MeV or PCAL> 300 MeV | 1
24 | Forward electron 1 forward and 1 central | FT (1800-6600) x DC x FTOFPCU x PCAL x CTOF | PCAL>15 MeV CTOF clusters>2 MeV | 1
25 | Forward electron 2 forward | FT (1800-6600) x (DC x FTOFPCU x PCAL x CTOF)2 | PCAL>15 MeV | 1
28 (new) | Forward electron 1 forward and 1 central | FT (1800-6600) x DC x FTOFPCU x PCAL x CTOF X CND | PCAL>15 MeV CTOF vs CND map no additional threshold | 1
Accept 13 kHz events @ 91% live time
RGA Service triggers from 7 to 18 and from 27 to 31 will also be in place .
No need for “muon” triggers 19-20-21

## Slide 3
Run Group K Triggers Configuration E=6.5 GeV
Trigger Number | Physics Definition | Detectors Conditions | Thresholds | prescale
0 | 1 electron in CLAS All sectors – with DC | (DC x HTTC x ECAL x PCAL) or (DC x HTTC x PCAL) | (PCAL+ECAL)> 300 MeV PCAL>60 MeV ECAL>10 MeV or PCAL> 300 MeV | 1
1-6 | 1 electron in CLAS Fixed Sector – with DC | (DC x HTTC x ECAL x PCAL) or (DC x HTTC x PCAL) | (PCAL+ECAL)> 300 MeV PCAL>60 MeV ECAL>10 MeV or PCAL> 300 MeV | 1
24 | Forward electron 1 forward and 1 central | FT (1800-5600) x DC x FTOFPCU x PCAL x CTOF | PCAL>15 MeV CTOF clusters>2 MeV | 1
25 | Forward electron 2 forward | FT (1800-5600) x (DC x FTOFPCU x PCAL x CTOF)2 | PCAL>15 MeV | 1
28 (new) | Forward electron 1 forward and 1 central | FT (1800-5600) x DC x FTOFPCU x PCAL x CTOF X CND | PCAL>15 MeV CTOF vs CND map no additional threshold | 1
Accept 13 kHz events @ 91% live time
RGA Service triggers from 7 to 18 and from 27 to 31 will also be in place.
No need for “muon” triggers 19-20-21

## Slide 4
Expected Data Volume and Events
 | Event | Beam-second | Week | 2018 Period – 9 PAC days
Row EVIO | 50 kB | 600 MB | 180 TB | 231 TB
Decoded Hipo | 13 kB | 195 MB | 59 TB | 75 TB
DST Hipo | 2.2 kB | 33 MB | 10 TB | 13 TB
Inputs: Ie = 75 nA (L = 1035 cm-2s-1)
Trigger rate = 12 kHz
 | Event | Beam-second | Week | 2018 Period – 9 PAC days
Row EVIO | 35 kB | 420 MB | 125 TB | 160 TB
Assuming data compression achieved -> x 0.7 event size reduction