## Slide 1
2018 Requested RG-K Experimental Set-up
Electron energies = 7.5 GeV and 6.5 GeV
Torus current = +100% negatives outbending
Solenoid Current = -100 %
Forward Tracker = No
Forward Tagger = Yes
Luminosity as high as possible, limited by acquisition rate up to 18kHz

## Slide 2
Run Group K Trigger Configurations E=7.5 GeV
Trigger Number | Definition | Detector Conditions | Thresholds | Prescale
0 | 1 electron in CLAS All sectors – with DC | (DC x HTCC x ECAL x PCAL) or (DC x HTCC x PCAL) | (PCAL+ECAL)> 300 MeV PCAL>60 MeV ECAL>10 MeV or PCAL> 300 MeV | 1
1-6 | 1 electron in CLAS Fixed Sector – with DC | (DC x HTCC x ECAL x PCAL) or (DC x HTCC x PCAL) | (PCAL+ECAL)> 300 MeV PCAL>60 MeV ECAL>10 MeV or PCAL> 300 MeV | 1
24 | Forward electron 1 forward and 1 central | FT (1800-6600) x DC x FTOFPCU x PCAL x CTOF | PCAL>15 MeV CTOF clusters>2 MeV | 1
25 | Forward electron 2 forward hadrons | FT (1800-6600) x (DC x FTOFPCU x PCAL x CTOF)2 | PCAL>15 MeV | 1
28 (possible additional trigger bit) | Forward electron 1 forward and 1 central hadron | FT (1800-6600) x DC x FTOFPCU x PCAL x CTOF X CND | PCAL>15 MeV CTOF vs CND map no additional threshold | 1
Accept 18 kHz events @ 93% live time
RG-A service trigger bits 7 - 18 and 27 - 31 will also be in place
No need for RG-A “muon” trigger bits 19-21

## Slide 3
Run Group K Trigger Configurations E=6.5 GeV
Trigger Number | Definition | Detectors Conditions | Thresholds | Prescale
0 | 1 electron in CLAS All sectors – with DC | (DC x HTCC x ECAL x PCAL) or (DC x HTCC x PCAL) | (PCAL+ECAL)> 300 MeV PCAL>60 MeV ECAL>10 MeV or PCAL> 300 MeV | 1
1-6 | 1 electron in CLAS Fixed Sector – with DC | (DC x HTCC x ECAL x PCAL) or (DC x HTCC x PCAL) | (PCAL+ECAL)> 300 MeV PCAL>60 MeV ECAL>10 MeV or PCAL> 300 MeV | 1
24 | Forward electron 1 forward and 1 central | FT (1800-5600) x DC x FTOFPCU x PCAL x CTOF | PCAL>15 MeV CTOF clusters>2 MeV | 1
25 | Forward electron 2 forward | FT (1800-5600) x (DC x FTOFPCU x PCAL x CTOF)2 | PCAL>15 MeV | 1
28 (possible additional trigger bit) | Forward electron 1 forward and 1 central | FT (1800-5600) x DC x FTOFPCU x PCAL x CTOF X CND | PCAL>15 MeV CTOF vs CND map no additional threshold | 1
Accept 18 kHz events @ 93% live time
RG-A service trigger bits 7 - 18 and 27 - 31 will also be in place
No need for RG-A “muon” trigger bits 19-21

## Slide 4
Expected Data Volume and Events
 | Event | Beam-second | Week | 2018 Period – 9 PAC days
Raw EVIO | 50 kB | 600 MB | 180 TB | 231 TB
Decoded HIPO | 13 kB | 195 MB | 59 TB | 75 TB
DST HIPO | 2.2 kB | 33 MB | 10 TB | 13 TB
Inputs: Ie = 75 nA (L = 1035 cm-2s-1)
Trigger rate = 18 kHz
 | Event | Beam-second | Week | 2018 Period – 9 PAC days
Raw EVIO | 35 kB | 420 MB | 125 TB | 160 TB
Assuming data compression achieved -> x 0.7 event size reduction