## Slide 1: CLAS12 L1-based Trigger System Upgrade Plan (draft for overall discussion)
S.Boyarinov, B.Raydo

## Slide 2
CLAS12 Existing Trigger System Hardware
Notes: HTCC – not “central” detector

## Slide 3: CLAS12 Trigger Overview
Current CLAS12 Level 1 trigger is based on information coming from two types of front-end boards: FADC250 (Flash ADC) and DCRB (Drift Chamber Readout Board)
FADC250s are used in HTCC, ECAL, PCAL, FTOF, CTOF, CND, FT_CAL and FT_HODO
DCRBs are used in Drift Chamber
L1 trigger consists of 3 stages and implemented using two types of specialized logic boards: VTP (stage 1 and 3) and SSP (stage 2); L1 trigger is fixed latency system with the latency less then 8us
Stage 1 receives initial hits from front-end boards and produces objects suitable for the following trigger stages; those objects includes calorimeter clusters, drift chamber roads, and hits from time-of-flight and Cherenkov counters
Stage 2 collects information from one CLAS12 sector and produces sector-based trigger decision
Stage 3 collects information from all sectors and central detectors, and delivers final trigger decision to Trigger Supervisor as 32 bit word every 4ns with pre-scaling for every bit
Every stage of the trigger system has flexible logic controlled by set of configuration parameters, allowing to specify energy cuts, timing coincidences, geometrical matches (DC-FTOF-PCALU, CTOF-CND, FT_CAL-FT_HODO so far), multiplicity and combinatorial logic

## Slide 4: CLAS12 L1 Trigger Possible Upgrades
ECAL/PCAL trigger can to be improved in following ways: (1) in addition to electron shower clustering, search for MIP-like clusters have to be added to improve muon class triggers; (2) use individual strip real attenuation length instead of average one; (3) allow individual strip timing delays and improve cluster timing reporting
DC trigger can be improved (needed in particular for Q**2 cuts) in following ways: (1) segments selectivity and space resolution improvement; (2) roads space resolution improvement; (3) drift time usage to improve two previous items feather
Additional geometry matching between detectors, for example DC vs PCAL clusters,
Allow multi-particle trigger in one sector
Improve trigger timing in every component and stage to straighten timing coincidence
See following slides for details on every item

## Slide 5: ECAL/PCAL Trigger Upgrade
in addition to electron shower clustering, search for MIP-like clusters have to be added to improve muon class triggers – it can be challenging, we have to conduct two cluster searches, one with highest energy and another with MIP energy; will try and see if it will fit into fpga; another solution can be to search for the MIP cluster only if DC track is present, in that case cluster assembly can be done around track hit point, independently of electron clustering search, however DC track info is not available at stage 1 where EC cluster search is conducted – all that needs to be studied
use individual strip real attenuation length instead of average one – can be done, it should improve cluster energy resolution and allows more precise energy cuts
allow individual strip timing delays and improve cluster timing reporting – can be done

## Slide 6: Drift Chamber Trigger Upgrade
segments selectivity and space resolution improvement: for offline reconstruction purposes, Mac suggested to modify DCRB to have multi-hit reporting in some form (‘time-over-threshold’ etc), if implemented it may effect trigger segment search; in general not much can be done on hit-based level to improve existing segment finder
roads space resolution improvement: with new unit with bigger fpga (see picture below) or/and road dictionary reorganization, single-cell dictionary can be used to improve space resolution, however dictionary incompleteness may require to use smearing (doing it now) and it will decrease resolution again; offline modeling is strongly suggested to study possible road dictionary improvements
drift time usage to improve two previous items further: if timing information is used, it can potentially improve segment search selectivity and precision, as for road finding; again, all remarks from previous item is applicable here, and in addition it is unclear how exactly to use hits timing – offline modeling is needed
AI approach should be tested for segment finding, especially with timing usage, it may be promising. Also for road finding to compare resource requirements vs dictionary approach

## Slide 7: Geometry Matching Upgrade
Additional geometry matching between detectors, for example DC vs PCAL clusters: it can be implemented on stage 2 (no need on stage 3 since we do not have cross-sector tracks); we may need to increase bandwidth from stage 1 to stage 2 to report required information for geometry match

## Slide 8: Muli-particle Logic Upgrade
Allow multi-particle trigger in one sector: it have to be considered in connection with DC stage 1 and geometry matching upgrades; in general, it should be relatively easy to count tracks matched for example with EC clusters and FTOF, but not practical to count tracks alone since road dictionary produces a number of solutions for the same track – needs to be studied

## Slide 9: Trigger Timing Upgrade
Improve trigger timing in every component and stage to straighten timing coincidence – as simple as this, just go though full logic chain and see where we can define timing more precisely

## Slide 10: Hardware Upgrade
The only hardware change will be needed if modified DC road finder will need bigger fpga, in that case we recommend to install new units (one per sector) between stage 1 and stage 2, with fiber connections to both; in that scheme existing DC Stage 1 can be designated for DC segment finding only – see following slide

## Slide 11
CLAS12 Trigger System Hardware Upgrade
New Road Finder
Notes: HTCC – not “central” detector

## Slide 12
CLAS12 Level3 for Extra Data Rate Reduction
Level 3 can provide additional data rate reduction, it is our strong recommendation to offline data processing community to identify packages which can be used in Level 3; DAQ infrastructure is ready, any an assistance in implementation will be provided
Level 3 is existing DAQ component,
running between Event Builder and Event Recorder, currently dummy
Notes: HTCC – not “central” detector