## Slide 1: HPS Engineering Run Update
HPS Collaboration May 19, 2015
Run 5623 Event 62 N. Graf

## Slide 2: HPS Setup in Hall B Alcove
Si Vertex Tracker Installed Feb 23, 2015
PbWO4 Ecal Installed September, 2014
A magnet chicane directs the CEBAF 12 electron beam onto a W foil, producing heavy photons. They decay to e+e- pairs, which are measured by the Si vertex tracker inside an analyzing magnet. A PbWO4 ECal provides a fast trigger. https://confluence.slac.stanford.edu/display/hpsg/Heavy+Photon+Search+Experiment
e-

## Slide 3
Beam’s Eye View of SVT

## Slide 4: Spring Engineering Run
Installed SVT end of February
Commissioned Hall B beamline March-April * Calibrated bpms & established orbit locks * Set up SVT Protection Collimator * Checked beam position stability
CEBAF down after power outage
Commissioned Trigger and Integrated SVT DAQ late April
Explored SVT backgrounds as moved SVT closer to beam
Production running at 1.5 mm started May 1
Production running at 0.5 mm started May 12
Layer 1 silicon sensors are just 0.5 mm above and below beam. Min opening angle is y= 15 mrad.
Run 5623 Event 62 N. Graf

## Slide 6: Tracked Pairs at 1.5 mm
A’ candidates have Pe+ + Pe-  Pbeam = 1.05 GeV
Plots from M. Graham

## Slide 7: Track Matching at Ecal
Alignment fine tuning needed, but close

## Slide 8: SVT Momentum/ ECal Energy Match
Further Ecal Calibration/Tracker Alignment Needed

## Slide 9: Pairs Vertex at the Target

## Slide 10: Pairs Mass Distribution

## Slide 11: Reach vs Runtime
1 GeV Contours:
1 PAC week 5/7 PAC week 3/7 PAC week
Assumes coverage to 15 mrad
Measurement assured, but no new territory

## Slide 12: Physics Measurement?
We have roughly 1/3 PAC week with Si at 0.5 mm (15 mrad acceptance)
Beamline, Ecal, Trigger and SVT all worked well
Lots of Work to Do… Check Trident Yield in the data Ecal energy calibration and alignment SVT alignment Understand the Vertex Tails
But a physics result may be in reach