## Slide 1: Photoproduction of 67Cu and 177Lu in Ga and Ta
Pavel Degtiarenko, George Kharashvili, JLab RadCon
8/7/15

## Slide 2: Motivation
Near-threshold cross-sections are poorly known
  Missing experimental data
  Models often fail
Radiological concerns
  Evaluation of activation at low energies
Medical isotope production
  ”Clean" process at lowest practical energies

## Slide 3: 67Cu
One of the most promising radioisotopes for cancer therapy
Promising in diagnostics as well
T1/2 = 2.87 d
  β- decay to stable 67Zn
  Produces 184.58 keV photon (Y = 48.7%)
  68Zn(γ,p)67Cu considered for photoproduction
We propose investigating 71Ga(γ,α)67Cu

## Slide 4: Photon induced reaction in Ga
Reaction | Threshold (MeV) | Product T1/2
71Ga(γ,α)67Cu | 5.25 | 61.83 h
71Ga(γ,n)70Cu | 9.3 | 21.1 min
69Ga(γ,n)68Ga | 10.3 | 67.6 min
69Ga(γ,α)65Cu | 4.48 | Stable
  Natural Gallium: 69Ga – 60%, 71Ga – 40%

## Slide 5: 177Lu
177Lu
  T1/2 = 6.73 d
  β- decay to 177Yb (T1/2=1.9h)
  Produces 208.4 keV photon (Y = 11%)
Possible production channel
  181Ta(γ,α)177Lu
  Eth = 0

## Slide 6: Cross-sections

## Slide 7
Average photon fluence in a 0.5”x0.5”x0.5” Ga sample 1cm downstream from a 6mm Cu radiator

## Slide 8: Expected Activation Rates
Beam Kinetic Energy (MeV) | Activity of 67Cu (Bq/h/10μA)
9.5 | 1.25
10 | 4
Folding the calculated spectra with the TENDL-2014 cross-sections would result in the following activation rates:
Expected dose rates - below detection limits of survey meters after several hour long irradiation. Standard procedure for removal of potentially activated items in place

## Slide 9: Gamma Spectroscopy
RadCon Radioanalytical Lab (ARC ground floor) operates a state of the art gamma spectroscopy system
  2 shielded HPGe detectors + 1 portable unit
  Several NIST traceable multinuclide standards
  1 of the shielded detectors and the portable unit are characterized for use with ISOCS/LabSOCS calibration software
Our activation analysis experience at JLab
  Foil activation study at g2p beam dump in Hall A
  C100 activation monitoring

## Slide 10: Detection Limits
67Cu detection limits evaluated using ~4h count of empty shield and by applying detection efficiencies calculated with LabSOCS for a 0.5”x0.5”x0.5” Ga sample