## Slide 1: Isotope Production at LERF
Pavel Degtiarenko
Radiation Physics Group at RadCon
September 8, 2015

## Slide 2: Processes
Processes to consider (the quick cost data are from Google)
  68Zn (0.05 $/g) (18% nat) (g,p) 67Cu (2.6d)
  71Ga (2.2 $/g) (40% nat) (g,a) 67Cu (2.6d)
  178Hf (1.2 $/g) (27% nat) (g,p) 177Lu (6.6d)
  181Ta (4.5 $/g) (100% nat) (g,a) 177Lu (6.6d)
  226Ra (100 k$/g) (100% nat) (g,n) 225Ra (14.9d) → 225Ac (9.9d)
  To limit choices of the processes and methods we need reasonable figures of merit for demand quantities of the isotopes to be produced:
  What would be the minimum amount of curies produced per day that is not too low to be usable and to satisfy demand?
  How much is too much to be realistically sold?
Need a list of parameters that could impose other limits, for example, limits on target (chemical) processing, transportation, safety, etc.

## Slide 3: Irradiation Methods to Consider (1)
Direct bulk irradiation by electron beam, thick targets
  Target thick enough to absorb up to ~80% of the beam power; it functions as a beam dump; must use the appropriate shielding
  Advantages:
    Largest “curie per joule” production parameter
    At higher energies easier conditions on the beam exit window
  Difficulties:
    Target cooling requirements
    Smaller average isotope densities produced
  Restrictions:
    Can’t be used for Radium (bulk targets not available)

## Slide 4: Irradiation Methods to Consider (2)
Two-stage irradiation setup
  Use of a dedicated cooled radiator, producing gamma beams, which irradiate the isotope production target downstream
  Advantages:
    Use of both thick and thin targets, optimization possible
    Significantly easier requirements on the target cooling, because most of the beam power is removed by the radiator and by the charged particle filter using magnetic field
  Difficulties:
    Significant portion of beam power is not used in production
    Big one-time effort on the design of the cooled radiator, shielding enclosure, remote target handling, possibly including the means for extra cooling of the target

## Slide 5: Beam Energy Considerations
One element of the optimization is beam energy selection
  Cross sections for the isotope production are generally peaked at about 15-20 MeV in (g,n), and at about 20-25 MeV in (g,p) and (g,a) reactions
  Photon spectra dependence on energy is proportional to (1/Eg) in thin radiators and targets, gradually transitioning to ~(1/Eg)2 for radiators/targets thicker than 2-3 radiation lengths.
  Generally, increasing beam energy above peak production energy increases the isotope yields. However, with energy increase new channels open for production of undesirable isotopes further removed from the parent nucleus.
  In 67Cu production such isotopes include 65Cu and 63Cu which are difficult to separate from 67Cu. To limit their production the photon spectrum might need to be limited at 30-35 MeV
  The same with production of stable 175Lu accompanying 177Lu. What apportioning would be acceptable?