## Slide 1: Isotope Production at LERF
Pavel Degtiarenko
Radiation Physics Group at RadCon
October 2, 2015

## Slide 2: FLUKA toy model geometry
Air volume, Tungsten radiator and dump, 226Ra target
Magnetic field volume 5x5x5 cm3
Radiator
Target

## Slide 3: Selected Results on 226Ra target
Beam 150 kW, 226Ra target - 1 Ci (=1 g)
Production of 225Ac after 1h irradiation & 18d decay
  150 MeV beam, 1 mm W radiator, 5 T x 5 cm magnetic field, 10 cm between radiator and target, 4 mm diameter target. Results: 13 mCi 225Ac produced, 3.7 kW in radiator, 620 W in the target
  50 MeV beam , 5 mm W radiator, no magnetic field, 2.5 cm between radiator and target, 6 mm diameter target. Results: 35 mCi 225Ac produced, 67 kW in radiator, 1.1 kW in the target

## Slide 4: High energy, thin radiator run
Colors represent dose rates in arbitrary units

## Slide 5: High energy, thin radiator run
Colors represent activities in mCi
226Ra (1600y) parent
225Ra (14.9d)
221Fr (4.9m)
225Ac
(9.9d)
217At (1.5s)
213Bi (46m)
213Po (164ms)
209Pb (3.2h)

## Slide 6: Medium energy, medium radiator run
Colors represent dose rates in arbitrary units

## Slide 7: Medium energy, medium radiator run
Colors represent activities in mCi
226Ra (1600y) parent
225Ra (14.9d)
221Fr
(4.9m)
225Ac
(9.9d)
217At (1.5s)
213Bi (46m)
213Po (164ms)
209Pb (3.2h)
209Bi
(stable)
for 1 hour

## Slide 8: 225Ac from 232Th target
Natural Thorium-232 (100% nat) is readily available at (~5 $/g)
Processes leading to 225Ac production:
Immediate (hours of irradiation to ~mCi production of 225Ac )
  232Th (g,6n+p) 225Ac (9.9d) - direct
  232Th (g,7n) 225Th (8.7m) → 225Ac (9.9d)
  232Th (g,5n+2p) 225Ra (14.9d) → 225Ac (9.9d)
  Delayed (~1000 hours of irradiation to ~mCi production of 229Th, to be used to produce ~mCi of 225Ac every ~20 days “forever”)
  232Th (g,3n) 229Th (7880Y) → 225Ra (14.9d) → 225Ac (9.9d)

## Slide 9: High Energy, thick Thorium target

## Slide 10: High Energy, thick Thorium target run
mCi
for 1 hour
232Th (1.4 1010y) parent nucleus

## Slide 11: High Energy, thick Thorium target run
232Th (1.4 1010y) parent
229Th
(7880y)
225Ra (14.9d)
225Th (8.8m)
221Fr
(4.9m)
225Ac
(9.9d)
217At (1.5s)
213Bi (46m)
213Po (164ms)
209Pb (3.2h)
209Bi
(stable)
mCi
for 1 hour
230Th (7.5 104y)
optional parent
if available

## Slide 12: Low Energy, thick Thorium target run
232Th (1.4 1010y) parent
229Th
(7880y)
225Ra (14.9d)
221Fr
(4.9m)
225Ac
(9.9d)
217At (1.5s)
213Bi (46m)
213Po (164ms)
209Pb (3.2h)
209Bi
(stable)
mCi
233Pa (27d)
230Th (7.5 104y)
optional parent
if available

## Slide 13: Medium Energy, thick Gallium target

## Slide 14: Medium Energy, thick Gallium target run
71Ga parent (40%)
67Cu
(61.8h)
mCi
for 1 hour
69Ga parent (60%)
64Cu (12.7h)
71Ga(2.2 $/g)(40% nat) (g,a) 67Cu

## Slide 15: Medium Energy, thick Tantalum target
181Ta parent (100%)
177Lu
(6.6d)
mCi
for 1 hour
Limited yield, but well isolated isotope 177Lu
  181Ta(4.5 $/g)(100% nat) (g,a) 177Lu

## Slide 16: Subsystems’ Critical Parameters
LERF accelerator beam current limit
  Machine limits, function of energy <?>
Vacuum Window: Beam current limit
  Design limits <?>
Radiator: Power density and Power deposition limit
  Design limits <?>
Target: Absorbed power limit
  Design limits <?>
  Isotope production limits <?>
Dump: Total beam power limit
  Should be no big problem

## Slide 17: Extras

## Slide 18
List of Processes
Natural Thorium-232 (100% nat) is readily available at (~5 $/g)
Processes leading to 225Ac production:
Immediate (hours of irradiation to ~mCi production of 225Ac )
  232Th (g,6n+p) 225Ac (9.9d) - direct
  232Th (g,7n) 225Th (8.7m) → 225Ac (9.9d)
  232Th (g,5n+2p) 225Ra (14.9d) → 225Ac (9.9d)
  Delayed (~1000 hours of irradiation to ~mCi production of 229Th, to be used to produce ~mCi of 225Ac every ~20 days “forever”)
  232Th (g,3n) 229Th (7880Y) → 225Ra (14.9d) → 225Ac (9.9d)
List of processes considered earlier
  68Zn (0.05 $/g) (18% nat) (g,p) 67Cu (2.6d)
  71Ga (2.2 $/g) (40% nat) (g,a) 67Cu (2.6d)
  178Hf (1.2 $/g) (27% nat) (g,p) 177Lu (6.6d)
  181Ta (4.5 $/g) (100% nat) (g,a) 177Lu (6.6d)
  226Ra (100 k$/g) (100% nat) (g,n) 225Ra (14.9d) → 225Ac (9.9d)

## Slide 19: Low energy, medium radiator run
Colors represent dose rates in arbitrary units

## Slide 20: Low energy, medium radiator run
Colors represent activities in mCi