## Slide 1: Production of 225Ac on 230Th Target at 12 MeV
Pavel Degtiarenko
Radiation Physics Group at RadCon
October 5, 2015

## Slide 2: Thorium-230
230Th may be separated from 238U decay products
Readily(?) available at DOE (Oak Ridge?)
Must be cheaper than 226Ra, and in larger volumes
Small intrinsic radioactivity
Large cross section 230Th (g,n) 229Th
229Th decays to 225Ra (half life 7880 years)
Time to regenerate 1 mCi of 225Ac from 1 mCi of 229Th, in equilibrium with 225Ra: ~18 days
At Eg < 12 MeV the production of accompanying radioactivity is small, some fission is present, no 233U generated
Proposal: to generate few mCi of 229Th once, and then extract 225Ac once every 18 days afterwards

## Slide 3: Test Setup
Standard technique for gamma irradiators:
  Use ~1 mm of W to generate “useful” gammas, and then place low-Z material (Be, Al) to stop electrons and to suppress low energy gammas
Test Setup: 1.2 mm W, 2.5 cm Be, 500 g 230Th
At 100 kW 12 MeV electron beam: radiator absorbs 50 kW, filter – 33 kW, and the target – 5 kW
Mechanically radiator and filter could be designed in a single device, or separately. The method of the rotating wheel, suspended in the flow of coolant can be implemented, as it was discussed in the proposal
Separate design for cooling the 230Th target is needed
Expected productivity: 1-2 mCi of 229Th in 1000 hours

## Slide 4: Test Setup
Radiator: W, 1.2 mm
Filter: Be, 25 mm
Target: 230Th, 500 g

## Slide 5: Results
The following two slides show activities of different radioactive isotopes produced in the 230Th target after running for 1000 hours in the Test Setup, using 12 MeV electron beam delivering 100 kW
Color of every square shows activity of the isotope AZ
When viewed in “Presentation Mode” every plot will show several distributions corresponding to different times after irradiation end, from 0 to 365 days
Activity of produced 229Th is about 2 mCi, activities of 225Ra and 225Ac come into equilibrium in 60-90 days
Activities of the fission products are significant during the irradiation and in the first hour after, but then decay fast

## Slide 6: Results: 229Th and its decay chain
229Th
(7880y)
225Ra (14.9d)
221Fr
(4.9m)
225Ac
(9.9d)
217At (1.5s)
213Bi (46m)
213Po (164ms)
209Pb (3.2h)
209Bi
(stable)
230Th (7.5 104y) parent

## Slide 7: Results: 230Th fission products

## Slide 8: Extras