## Slide 1
Requirements:
Must fit in vault and allow shielding around it.
Vault has shielding for 400 W at a location
Handle ebeam power: approx 50 kW? Extract heat and deal with ebeam.
1 to 1.5 mm tungsten window in front
Interface somehow with beamline vacuum (use Be window?)
Allow liquid Gallium perhaps 10 cm long diameter minimum TBD by allowed ebeam fluence. Minimize gallium volume with constraint of specific activity TBD. Another constraint: total activity above some number TBD.
Gallium easily removed after irradiation (and presumably installed initially.
Material compatibility with Ga, Cu.
Low copper content in container(s) so as to minimize cross contamination.
Remote target handling: suggest pour Ga in and then dump it out.?
Radiation damage minimized for long term survival. No gaskets, O-rings, embrittled materials.

## Slide 2
Actions and Comments:
Calculate how small the ebeam can be: 2 MeV/gm-cm^2 absorption times the current. Is limit tungsten radiator or Be window? Assigned: Gubeli
Vacuum window to beamline: is it needed (what is it?) Assigned: all
Is vacuum window thin or do we use it as the radiator?
Questions on specific materials: beryllium oxide ceramic? Silicon? What are material compatibilities? Sticks to glass. Not to poly. Need to investigate or add test to proposal tasks. Assigned: Areti, all
COMMENT: Two big questions: Extract heat from target. Contamination.
Can tungsten be pure enough so it doesn’t contaminate Gallium? If not can we use liner of TBD? Silicon?
COMMENT Focus beam going in so focal point is half way through Gallium
COMMENT: Want to make sure Ga doesn’t stick on everything because we don’t want to leave behind product and we may use isotopically pure material. can live with modest coating if it doesn’t getter copper and we re-use container.
What are possible concepts for remote handling? Dump it? A valve? Blow out the volume. Assigned: Jordan, Biallas, Gubeli all to consider.

## Slide 3
Action:
Consider working on the solid plug? Solid/liquid drain? How much sticks to tungsten? Is a weak acid flush reasonable? How much copper sticks there?
Does a tapered plug seal? : What tests do we need to do? Test wetting and seal of tungsten against tungsten. Assigned: Jordan to test sealing of tungsten plug.
What about powder form? Can we get good thermal contact?
What is optimum beam diameter/radiation cone to design for? Review George K’s analysis.
Is it better to separate the radiator so that it can be separately cooled? Assigned: Gubeli to consider in design
Does a poly catheter work to remove Ga? Need to get poly tube with no copper in it. Must be kept in clean environment? Need to rinse? Assigned: Gubeli to consider in design
How much is copper-free tungsten?
Measure purity of 3D printed tungsten. Assigned: Jordan to bring to ODU

## Slide 4
Simple cylinder vertical axis: simple concept shows power can be handled. Other configurations possible and may be optimal
Believe can handle power.
How to fill/empty
Liner or capsule for gallium?
Plug to drain?
Extract solid form
Use Ga oxide powder?
Orient vertically (room to point beam down? Requires 2 kG-m magnet; seems to be possible
Optimum Ga and other dimensions?
Separate radiator for easier cooling/vacuum interface?
Enclose in outer container to keep air away? N2 fill?
Cooling
Tungsten
Thermal conductor
Gallium
Comments: