## Slide 1
Isotope Production at LERF
Andrew Hutton
Jefferson Lab
for
  Hari Areti, Pavel Degtiarenko, Joe Gubeli, Kevin Jordan, George Kharashvili, George Neil Jefferson Lab
  Sundaresan Gobalakrishnan, Jamal Zweit Virginia Commonwealth University
  Doug Wells New Mexico Tech
AccApp’17 Quebec City August 1, 2017

## Slide 2: JLAB Low Energy Recirculator Facility (LERF)
LERF is an Energy Recovery Linac
World’s first high power FEL
Still holds power records for FEL and ERL operation
2
Beam accelerated from 9 to 170 MeV and then decelerated back to ~10 MeV, to recover the energy

## Slide 3: LERF Capabilities
The ERL in the LERF is available for:
  Fixed target experiments at medium current
  Internal target experiments at high current
  Offline accelerator research and development
  Diagnostic development
  FEL studies in the IR and UV
  THz production
    Parameter Maximum value
    Current (ERL) 8 mA
    Energy 170 MeV
    Charge 150 pC
    Frequency 75 (750) MHz
    Current (fixed target) 0.5 mA

## Slide 4: Jefferson Lab for Isotope Production
Low Energy Recirculator Facility (LERF) is proposed for isotope production in non-ERL mode
  Up to 150 MeV energy electron beam
  Up to 100 kW beam power

## Slide 5: Schematic of ERL-Based Isotope Production
Presentation by Rol Johnson in Radio-Isotope-1 Session on Tuesday
LERF can also produce isotopes in ERL mode

## Slide 6: NSAC Isotopes Recommendations on Isotope R&D
“Continue support for R&D on the production of alpha-emitting radioisotopes”
“Support R&D into the production of high specific activity theranostic radioisotopes”
“Continue support for R&D on the use of electron accelerators for isotope production”
“Support R&D on the development of irradiation materials for targets that will be exposed to extreme environments to take full advantage of the current suite of accelerator and reactor irradiation facilities”
This study addresses all of these

## Slide 7: Isotope Production Collaboration
Jefferson Lab:
Hari Areti, Pavel Degtiarenko, George Kharashvili, Joe Gubeli, Kevin Jordan, George Neil
  Radiation physics, health physics, Monte-Carlo modeling, radiation metrology, high-power SRF electron accelerators, targetry, beam diagnostics, beam dumps
Virginia Commonwealth University:
Jamal Zweit, Sundaresan Gobalakrishnan
  Radiochemistry, radiopharmaceuticals, medical imaging, nanotechnology
New Mexico Tech:
Doug Wells
  Photonuclear physics, activation analysis, isotope production

## Slide 8: Recent Activities
2012 – Proposal for isotope production using LERF in ERL configuration submitted to DOE Isotope Program
  not funded (DE-FOA-000743)
2015 – Pre-R&D Proposal Funded by DOE Isotope Program
2015 – White paper for photoproduction of 67Cu
2016 – R&D proposal for 67Cu production – DOE Isotope Program
  not funded in 2017, under consideration for 2018 funding (DE-FOA-0001588)
2017 – US patent application: 67Cu Photoproduction in Gallium
2015/2017 – Proof of concept studies
  67Cu production in gallium and zinc targets at CEBAF injector
  67Cu separation from gallium at VCU

## Slide 9: 67Cu for Targeted Radiotherapy
Theranostic radionuclide
  141 keV mean energy β- for therapy (range in tissue is about a cell diameter)
  185 keV energy γ for SPECT imaging
  Can be paired with 64Cu for PET imaging
Near-ideal half-life of 61.8 hours
  Convenient for production, transportation, and delivery to patient
  Same order as biological half-life of copper and zinc (67Cu decays to stable 67Zn)
Favorable biochemistry – approved for human trials
  Not a bone or an organ seeker
  Not acutely toxic – both copper and zinc are essential trace nutrients

## Slide 10: Demand and Availability of 67Cu
  Historical lack of an adequate and reliable supply has impeded the development of 67Cu applications
Estimate of potential long-term US demand based on treating half of all new Non-Hodgkin Lymphomas gives ~12,000 Ci / year Smith, Bowers, Ehst, “The production, separation, and use of 67Cu for radioimmunotherapy: A review“, Applied Radiation and Isotopes 70 (2012) 2377–2383
67Cu is currently produced at:
  Brookhaven National Laboratory: Proton irradiation of zinc, produced periodically, ~60% of activity upon delivery is composed of 64Cu
  Argonne National Lab LEAF: Photoproduction reaction producing 100 mCi batches on demand, expandable to 2 Ci batches
  Idaho Accelerator Center: Photoproduction in zinc up to 10s of mCi / week, not intended for human use
Higher specific activities and improved radiological purity are desired

## Slide 11: Photoproduction of 67Cu in Gallium via 71Ga(γ,α)67Cu (1)
Gallium has favorable properties for high power targets
  ✔ Low melting point of 30 °C
  ✔ High boiling point of 2204 °C
  ✔ Low vapor pressure
  ✖ Corrosive to metals except tungsten and tantalum
50 kW irradiation of a Gallium target once per week will produce*
  100s mCi of 67Cu per week in natural gallium
  > 1 Ci/week in 71Ga (40% of natural Gallium)
  Typical medical dose of 67Cu – order of 10 mCi
  * Yields are calculated using FLUKA and scaled with data

## Slide 12: Photoproduction of 67Cu in Gallium via 71Ga(γ,α)67Cu (2)
Modest cross-section of 71Ga(γ,α)67Cu reaction can be compensated by high beam power and a thick target
Koning et al. "TENDL-2015: TALYS-based evaluated nuclear data library” https://tendl.web.psi.ch/tendl_2015/tendl2015.html

## Slide 13: Photoproduction of 67Cu in Gallium via 71Ga(γ,α)67Cu (3)
Beam Pipe
50 kW Electron beam
High-Z Radiator
Coolant flow
Cooling Jacket
Target container
Bremsstrahlung photons
Liquid gallium
Coolant lines
Isotope production

## Slide 14: Overall Objectives and First Steps
The overall objective is to integrate
  Production
  Chemical Separation
  Delivery
First (opportunistic) steps
  Confirm 67Cu production in gallium
  Chemically separate 67Cu from gallium
  Investigate 67Cu delivery mechanisms

## Slide 15
Irradiation of Gallium and Zinc targets during beam studies in CEBAF injector:
  18.5 MeV (to avoid interference from 67Ga), 2.5 µA, 1 h
  ~ 0.1 µCi 67Cu detected in each target
First Opportunistic Irradiation Test
1mm Tungsten radiator
Natural Zinc target
Natural Gallium target
Boron Nitride crucible
Beryllium window
Kapton tape to prevent Gallium spills

## Slide 16: Chemical Separation Test
Chemical separation test at Virginia Commonwealth University (VCU)
  1 mCi of 67Cu was obtained from the National Isotope Development Center
    Shipped from BNL to VCU
  The sample was dissolved in hydrochloric acid and added to gallium chloride in solution
  Separation by liquid-liquid extraction and column chromatography recovered ~95% of the radioactive copper after a single pass

## Slide 17: Second Opportunistic Irradiation Test (1)
During 2017 beam studies of 4K operation in CEBAF injector, there was a parasitic opportunity for isotope irradiation
  85 g gallium target irradiated for several hours at 18.65 MeV, 50 µA (~1 kW) with the goal of chemically separating 67Cu
Beryllium Window
Tungsten radiator
Hexagonal Boron Nitride Capsule
Gallium Target

## Slide 18: Second Opportunistic Irradiation Test (2)
Due to failure of monitoring instrumentation, run was terminated earlier than anticipated
~130 µCi 67Cu was produced, ~70 µCi was available at the time of sample retrieval (aimed to produce ~500 µCi)
Due to transportation and communication issues did not proceed with chemical separation
The two, low-energy irradiation tests showed reasonable agreement with the model predictions
  FLUKA (our primary tool for activation calculations) appears to overestimate 67Cu yields in Gallium by approximately a factor of 2 at 18.5 MeV maximum bremsstrahlung energy

## Slide 19: Summary and Proposed Future Work
67Cu production via the 71Ga(γ,α)67Cu reaction at LERF: Production of high specific activity, theranostic isotope using a high-power electron accelerator
  Measured photoproduction of 67Cu at low energies (< 20 MeV)
    No 64Cu content detected
  Chemically separated 67Cu from Gallium
    Obtained from BNL, then dissolved in Gallium
  Proposed future work
    Complete smooth integration of photoproduction and chemical separation
    Produce 67Cu in Gallium target at optimal electron beam energies (> 30 MeV)
    Develop high power target system
Investigate photoproduction of α-emitters
  225Ac production in 226Ra, 230Th, 232Th targets