## Slide 1: LERF Cryomodule Shuffle
Kevin Jordan Sep. 15, 2017

## Slide 2: Scope
  Secure vacuum on all three modules
  Remove the three girders between FL03 & FL04
  Sample beam tube from above for contamination
  Remove girders as needed between FL02 & FL03 to enable move of F100 in FL02
  Remove F100 (FL02), and SL21 (FL03)
  Warm-up and move C50 (FL04) to FL02
  Reconnect cryo & RF to C50 in FL02
  Summary/Questions/Concerns/Comments

## Slide 3: LCLS-II CM Layout in LERF – Testing 2 CMs per Cycle
Current machine contains slots for 3 full CMs and 1 Injector CM
Shielded vault
Existing PSS including radiation and ODH monitoring
Utilities include cryo, water, electrical
Propose 2 CMs installed in middle of FEL machine
CM Slot
CM Slot
CM Slot
Access
Storage

## Slide 4: End Can & U-tubes – Conceptual Design
Relief Stack, Valves and Cooldown Line Connection
End Can, Mounted to Floor
Interconnect Bellows with Restraints
Return Line
Return TL
Supply Line
Supply TL
Re-use existing U-tubes for cryo connection
Stands w/Wheels
Floor Plates
Uses both FL03 & FL04 taps

## Slide 5: FL03/04 – clear out completely

## Slide 6: FL02/03
Remove & replace as needed to move CM FL02
Restore girder & vacuum with valve on downstream end

## Slide 7: C50 – Replace Ion Pump?
Take opportunity to replace pump…

## Slide 8: LCLS-II CM Layout in LERF – Testing 2 CMs per Cycle
~1 m OD x 12 m Long, Handling weight 8 tons max
End Can, New Design
End Cap, Existing Design
Interconnect w/
Beamline connection and Cryo line flanged connections