## Slide 1: MOLLER Spectrometer Downstream Coil Design Down Select - The Process
R. Fair
v1.00 – 12.02.20 – First Release
(with support from the JLab Magnet Group, J. Mammei, K. Kumar and others)

## Slide 2
Introduction to the two DS coil designs
How do we use the Pugh Matrix?
Extract from the matrix for the coil down select
What happens next…….?

## Slide 3
Introduction to the two DS coil designs
DS Hybrid Torus: Co-wound coils
DS Segmented Torus: Independent coils

## Slide 4: Coil Engineering - Process
Choose appropriate design goals [1]
  Current density: 20 A/mm2
  Water Flow Velocity: 15 ft/sec
  Water temperature rise: 35 oC ( note coolant supply 30 oC)
Choose a operating differential pressure 100 psid (chosen to allow increase if needed to create flow but not limiting fitting or hose type choice)
Nominal Current (Ampere Turns) by zone provided by collaboration)
Design current is 110% of nominal value provided by the collaboration
Choose a conductor size (H x W x dia) for each coil type and create wind-able design to match collaboration requested current placement geometry and to clear particle tracks
Provide simplified (blocky model) of winding layout to collaboration for evaluation of particle tracking
Magnet type | US | Zone 1 | Zone 2 | Zone 3 | Zone 4
Hybrid | 5358 | 7752 | 10602 | 16862 | 29160
Segmented (15% More than Hybrid DS coil) | 5358 | 8914 | 12192 | 19391 | 33534
[1] – Based on review of water-cooled magnets at JLab and SLAC
Notes: Go through bullets
Not Segmented needs 15% more current due to reduced coil straight lengths

## Slide 5
What is a Pugh Matrix ?
It is a framework which formalizes decision-making
It allows us to identify the strengths and weaknesses of one solution compared to another
It also allows us to record how we made the decision
It works best when the whole team participates

## Slide 6
How do we use the Pugh Matrix – this MUST be a team effort
Enter Critical to Quality (CTQs) requirements
  For the Moller spectrometer, the main requirement (obviously) is being able to perform the physics
    This top level requirement can be broken down further to include the engineering requirements. We have divided it into DESIGN, FABRICATION, ASSEMBLY and OPERATION
Give each CTQ a weight – i.e. ask ourselves how important is each CTQ to satisfying the physics requirements? The weights are usually rated from 1 to 10.
Rate each alternative design as better (1), worse (-1) or the same (0) as the ‘baseline design’.
  Here we have selected the ‘baseline design’ to be the Hybrid coil design and the segmented coil design as the alternative

## Slide 7
Extract from the Pugh Matrix for the coil design down select
X

## Slide 8
Extract from the Pugh Matrix for the coil design down select

## Slide 9
Extract from the Pugh Matrix for the coil design down select

## Slide 10
What happens next…….?
All team members to review the Pugh Matrix Excel Worksheet (in particular the weights) – by Friday 4th Dec
Friday 4th Dec – detailed review of the Pugh Matrix  make the down select
Write a report summarizing the decision – Ruben, Juliette, KK
Convene the Change Control Board (by 12.15.20 ?) – Jim Fast
Present and defend the decision – Ruben, Juliette, KK
Formalize the decision – Jim Fast

## Slide 11
BACKUP – SYSTEM OVERVIEW

## Slide 12: Subsystem Overview
Extent of Spectrometer Scope + beam pipes to the dump
UPSTREAM
DOWNSTREAM
Scattering Chamber and Target
(not included in Spectrometer scope)
1.03.06 Blockers #6 and #7
(for calibration and background checks)
1.03.06 Collimator #1
(Primary beam intercepting collimator)
1.03.06 Collimator #2
(Primary acceptance defining collimator)
1.03.06 Collimator #4
(Secondary acceptance defining collimator)
1.03.02 Downstream Torus
(Focusing and separation of particles)
1.03.06 Collimator #5
(Photon-blocking collimator) and Lintels
1.03.07 Downstream Beam Pipes and Windows
Not shown here:
1.03.04 Field measurement system
1.03.05 Water chiller
1.03.08 Shielding supports
1.03.03 Upstream Torus
(Pre-bending of particles)
[Note: There is no Collimator #3]
Electron beam
Detectors
(Not included in Spectrometer scope)
Target Lead Wall
Hybrid Lead Wall
Lead Collar
Lead Collar
Drift Pipe
Detector Pipe
Drift Pipe
Lead Collar
Shield Pipes
Primary beam window

## Slide 13
BACKUP – KPPs

## Slide 15
BACKUP – Coil Hydraulic and Electrical Design
O:\Magnet_Design_Tools\Magnet Projects\MOLLER - Hall A\6. Engineering Calculations-Analyses-Simulations\Mechanical\Coil DP calcs
Filename: CDT 110percent - Sept 2020 100psi w_KPP Seg SC 4.xls
Worksheet: Release Sheet_V2

## Slide 16
UPSTREAM

## Slide 17
HYBRID DS

## Slide 18
HYBRID DS

## Slide 19
SEGMENTED DS

## Slide 20
SEGMENTED DS
5 turns per pancake
4 turns per pancake

## Slide 21
BACKUP – Clearances to Particle Envelopes
O:\Magnet_Design_Tools\Magnet Projects\MOLLER - Hall A\5. Preliminary Drawings - uncontrolled\Beamline Cad\ENVELOPE CLEARANCES
Filename: COIL CLEARANCES 2_RRW_dk.xlsx
Worksheet: Nov 2020

## Slide 22
UPSTREAM TOROID
DOWNSTREAM TOROID
SC1
SC2
SC3
SC4

## Slide 23
UPSTREAM

## Slide 24
DOWNSTREAM – SC1

## Slide 25
DOWNSTREAM – SC2

## Slide 26
DOWNSTREAM – SC3

## Slide 27
DOWNSTREAM – SC4