## Slide 1: Thoughts on Traceability in SRFOPS
26-Apr-2021
DRAFT- for Discussion

## Slide 2: Why do we have Serialization ?
There are many reasons why we have serialization in SRF
To maintain control over fabrication & test data and to track processes as they are completed on the floor
For Scientific reasons , and where certification (materials, pressure vessel etc.) is required
ISO 9001 requires that the organization controls and manages traceability
  – note that it is up to the organization to decide what needs traceability
For reference Section 8 of ISO 9001 ; 2015
8.5.2 Identification and traceability
The organization shall use suitable means to identify outputs when it is necessary to ensure the conformity of products and services. [Project Management, less of Operations Planning]
The organization shall identify the status of outputs with respect to monitoring and measurement requirements throughout production and service provision. [Operations Planning, less of Project Management]
The organization shall control the unique identification of the outputs when traceability is a requirement, and shall retain the documented information necessary to enable traceability.

## Slide 3: Software Hierarchy & limitations Pansophy is organized by Projects – presently not designed to use components across projects
What works
  SNs auto-populate after coding completed provided SN are entered at the start
What must be done manually
  New components (example fabricated parts )
  Parts delivered to SOTRs rather than Inventory
  Parts from other cryomodules
What will “break” the system
  Entering SN at later travelers must be done manually, (example no SN in Disassembly Travelers
  Anyone by passing Inventory and taking parts to the floor
SN from PRIMeS
Inventory Traveler
SN recorded in
Disassembly Traveler
SN for New Part
Fabrication Traveler
SN Auto-populate
WFO – across all CMs
CEBAF limited to specific CM
Serial Numbers should be entered at the Start

## Slide 4: Management of Large numbers of components across WFO (SNS, L2 etc) Projects
WFO Projects Traveler are auto populated (after coding)
  Components are procured – and SN are recorded in Inventory Travelers
    All other travelers are auto populated from PRIMeS
    Inventory Traveler captures vendor documentation
  SN are selected & recorded in the final assembly travelers
    Note that for WFO are able to use components across cryomodules
However even for WFO problems are starting :
  HE attempting to use LCLS_II Components such as cavities, Field Probe feedthroughs etc.

## Slide 5: However CEBAF Projects are a challenge
SW has Limitations
CEBAF Projects SN can only be entered by individual Cryomodule
To Auto populate SN must be codes and entered in
  Inventory Traveler (if a new part)
  Disassembly Traveler
Other sources SN must be manually entered if from
  Fabrication Traveler , Example New Dog Leg or WG
  Parts taken from another Cryomodule where they are common
    Inner Adapter, End Dish, Elbows, Dog Legs etc.
Possible solution to common parts – do the same as for WFO
WFO example SNS CM-01, CM-02
Energy Reach “project” for C50R, C75-01, C75-02 etc, instead of individual Projects by CM
Inserting SN Mid Process “breaks “ the SW

## Slide 6: Options for CEBAF
All SN Must have SN entered in Disassembly, Fabrication & Inventory Traveler
Option 1: Continue with existing system where each CEBAF CM has a separate project and therefore separate set Travelers
  Disadvantage
    Any shared common part must be entered or copied over manually
    Parts not labeled with Project Names cresting confusion in tracing to the right CM
Option 2: Create Higher level project similar structure to WFO for “Energy Reach” so all of the Cryomodules (example C75-01, 02 etc.) to allow for sharing of common parts across projects
  Advantages fewer travelers and greater ease for sharing parts ….
  Disadvantages
    significant for changes needed to Pansophy SW ……
    Some travelers will need to be re-written and/or reviewed

## Slide 7: Back- Up

## Slide 8: For Reference Common parts used across CEBAF
Component /Project |  | C20 | C50 (10 CMs ) | C50R | C75 | Nb3SN | C100 | C100R | P1 | F100
Cavities | Description | C20 |  | C20 | C75 - 5 Cell | C75-5 cell Nb2SN | C100 | C100 | C100 | C100
 |  |  |  | C50R-CPR-INSP-CAV | C75-CAV-INSP | NB3SN-INSP-CAV |  |  |  | 
 | Part No |  |  | no dwg | JL0059982- Rev A | JL0059982- Rev A |  |  |  | 
Inner Adapter | Description | C20 |  | C20 | C20 | C20 |  |  |  | 
 | Insp Traveler |  |  | C50R-CPR-INSP-INAD | C75-CPR-INSP-INAD | NB3SN-INSP-INAD |  |  |  | 
 | Part No | 11151-C-0075 (RevC-1990) |  | 11151-C-0075 (RevC-1990) | 11151-C-0075 (RevC-1990) | 11151-C-0075 (RevC-1990) |  |  |  | 
Dog Leg/Window/WG Assy | Description | Straight |  | Bent | Bent | Bent |  |  |  | 
 | Insp Traveler |  |  | C50R-CPR-INSP-DGLG | C75-CPR-INSP-DGLG | NB3SN-INSP-DGLG |  |  |  | 
 | Part No | CRM-088-2025-002 Rev B |  | CRM-088-2025-002 Rev C | CRM-088-2025-002 Rev C | CRM-088-2025-002 Rev B |  |  |  | 
Elbows | Description | C20 |  | C20 | C20 | C20 |  |  |  | 
 | Insp Traveler |  |  | C50R-CPR-INSP-HOME | C75-CPR-INSP-HOME | no Traveler ? |  |  |  | 
 | Part No | 11151-D-0002 (Rev.B-1990) |  | 11151-D-0002 (Rev.B-1990) | 11151-D-0002 (Rev.B-1990) | 11151-D-0002 (Rev.B-1990) |  |  |  | 
HOM Loads | Description | C20 |  | 2015 C75 Style | 2015 C75 Style | 2015 C75 Style |  |  |  | 
 | Insp Traveler | Orginal Dwg -1990 |  | C50R-CPR-INSP-LOAD | C75-CPR-INSP-HOML | NB3SN-INSP-HOML |  |  |  | 
 | Part No | 11151-B-0092 |  | JL0024622 | JL0024622-Rev B | JL0024622-Rev B |  |  |  | 
End Dish/Bellow Assy | Description | C20 |  | C20 | C20 | C20 |  |  |  | 
 |  |  |  | C50R-CPR-INSP-ENDD | C75-CPR-INSP-ENDD | NB3SN-INSP-ENDD |  |  |  | 
 | Part No |  |  | 11151-C-0219 | 11151-C-0219 | 11151-C-0219 |  |  |  | 
Helium Vessel | Description | C20 |  | C20 | C20 | ?? |  |  |  | 
Vac Vessel | Description | C20 |  | C20 | C20 | ?? |  |  |  | 
12 GEV Guard Vac WG |  |  |  |  |  |  | 12 GEV Guard Vac WG | 12 GEV Guard Vac WG | P1 Guard Vacuum Waveguide Inspection | 
 |  |  |  |  |  |  | C100-CM-INSP-GVWG | C100R-CM-INSP-GVWG | P1-INSP-GVWG | 
 |  |  |  |  |  |  | SOW-CRM-120-7000-S-1022-RevA | SOW-CRM-120-7000-S-1022-RevA | SOW-CRM-120-7000-S-1022-RevA |