Second iteration on positron capture solenoid
Jay Benesch
4 December 2023

Discussion

Concern about the positron beam emerging magnetized from the conversion target at a recent Ce+BAF meeting led me to add to the model a compensation solenoid before the target to null the field at the target. After a discussion with Andriy Ushakov, the center of the compensation solenoid was placed 10 cm before the conversion target. Current density in the capture solenoid had to be increased 11.5% to maintain the 1.3T central field given presence of the upstream magnet with opposite polarity. Current density remained within range previously considered so cooling estimates were not repeated. A field map with this configuration was generated and provide to Andriy. This work was done with the 25 cm IR iron on the capture solenoid rather than the 20 cm IR I prefer, per Andriy's request.

The compensation solenoid was assumed to use the same conductor as the larger one, in this case six turns by eight layers of 15 mm square insulated conductor. IR of the small solenoid is 7.5 cm to keep strain on the conductor to 10%. With 10 cm spacing it would not be possible to drive the two in series, shunting under 20 A from the smaller magnet to adjust its field as we do in CEBAF. I iterated on the Z at the center of the compensation magnet, ending at 10.16 cm (4”). This model has 0.1% less J in the smaller solenoid so a standard CEBAF shunt supply will work.

Figure 1. Model with compensation solenoid centered at Z=-60.16 cm. Capture solenoid center at Z=0, conversion target assumed at Z=-50.

The field is not precisely nulled in the model at Z=-50, see Figure 2, but is sufficiently close that one could adjust spacing and current to get the desired field at the tungsten target. The BH curve of the iron will affect fields enough that there is no reason to tweak more. Opera's Default “good magnet steel” BH was used in this model. The BH curve derived from JLab magnet performance is slightly different.
Figure 2. Field on a 5 cm radius disk at Z=-50 cm. Span [-10,16] Gauss.

Figure 3. Bz(0,0,Z) with compensation solenoid
Figure 4. Same as figure 3 except I've divided it into three regions: [-50,0], [0,50] and [50,100]

[-50,0]
Integral: 388659
Maximum: 12958.9 (X at maximum: 0)
Minimum: -9.57069 (X at minimum: -50)

[0,50]
Integral: 401565
Maximum: 12958.9 (X at maximum: 0.1)
Minimum: 1443.85 (X at minimum: 50)

[50,100]
Integral: 17464.4
Maximum: 1443.85 (X at maximum: 50)
Minimum: 54.2845 (X at minimum: 100)

∫B for Z=[0,100] is 7.8% above that in the region before. My understanding of magnetized particle beams is not sufficient to say whether this will be an issue.

Conclusion

It is possible to compensate the field of the capture solenoid so the positrons are created in near-zero field. The spinning copper rotor with tungsten target will still generate eddy currents. Positrons will emerge from the capture solenoid with net angular momentum.