## Slide 1: Data Quality and Analysis Status of PRad Experiment at Jefferson Lab
Weizhi Xiong
Duke University
For the PRad Collaboration
Spokespersons: A. Gasparian(contact person), D. Dutta, M. Khandaker, H. Gao
APS April Meeting 2017
January 28th, 2017

## Slide 2: Outline
Proton charge radius puzzle and PRad experiment
PRad experimental apparatus
Data quality and current status
Summary

## Slide 3: Proton Charge Radius Puzzle
Electronic measurement (ep elastic + ordinary H spectroscopy) v.s. muonic measurement (muonic H spectroscopy)
p Lamb shift measurements by CREMA (2010, 2013)
  Unprecedented precision, <0.1%

## Slide 4: Proton Charge Radius from ep Elastic Scattering
e-
e-
p
p
GE ,GM
Elastic ep scattering, in the limit of Born approximation (one photon exchange):
Structure-less proton:
GE and GM can be extracted using Rosenbluth separation
For PRad, cross section dominated by GE
Taylor expansion of GE at low Q2
Derivative at low Q2 limit

## Slide 5: PRad Experiment Overview
PRad goal: Measuring proton charge radius using ep elastic scattering
Unprecedented low Q2 (~2x10-4 GeV2)
  Fill in very low Q2 region
Large Q2 range in a single setting
  ~2x10-4 - 6x10-2 GeV2
Calibrate to the simultaneously measured Møller scattering process
  best known control of systematics
Aims to extract cross section and radius to sub-percentage level

## Slide 6: PRad Experiment Overview
PRad goal: Measuring proton charge radius using ep elastic scattering
Unprecedented low Q2 (~2x10-4 GeV2)
  Fill in very low Q2 region
Large Q2 range in a single setting
  ~2x10-4 - 6x10-2 GeV2
Calibrate to the simultaneously measured Møller scattering process
  best known control of systematics
Aims to extract cross section and radius to sub-percentage level
Mainz low Q2 data set
Phys. Rev. C 93, 065207, 2016

## Slide 7: PRad Experimental Apparatus
Data taking in May and June of 2016 in Hall B at Jefferson Lab, with 1.1 and 2.2 GeV electron beams
Over 1.3 billion events taken with hydrogen target

## Slide 8: PRad Experimental Apparatus
Electron Beam
8 cm dia x 4 cm long target cell
2mm holes open at front and back kapton foils, allows beam to pass through
Areal density: ~2 x 1018 H atoms / cm2

## Slide 9: PRad Experimental Apparatus
5m long two stage vacuum box, further remove possible background source
vacuum tank pressure: 0.3 mtorr

## Slide 10: PRad Experimental Apparatus
Two large area GEM detectors
Small overlap region in the middle
Excellent position resolution (~72µm)
Improve position resolution of the setup by > 20 times
Similar improvement for Q2 determination at small angle

## Slide 11: PRad Experimental Apparatus
Hybrid EM calorimeter
  Inner 1156 PWO4 modules
  Outer 576 lead glass modules
5.8m from the target
Polar angle coverage: ~ 0.6˚ to 7.5˚
Azimuthal angle coverage: 2π
High resolution and efficiency

## Slide 12: HyCal Resolution and Efficiency
HyCal energy resolution and trigger efficiency extracted using high energy photon beam from Hall B at Jlab
  > 99.5% trigger efficiency obtained for E𝜸 > 500 MeV, for various parts of HyCal
  Energy resolution ~2.6% for PWO4 part, lead glass part able 2.5 time worse
Preliminary
Preliminary

## Slide 13: Performance of GEM Detectors
GEM detection efficiency measured in both photon beam calibration (pair production) and production runs (ep and ee)
Using overlap region of GEMs to measure position resolution (~72𝛍m)
More details see presentation of X. Bai in session E12
100
90
80
70
60
Preliminary
Very Preliminary
Detection efficiency

## Slide 14: PRad Data Analysis Status
HyCal calibration accomplished with tagged photon beam and majority of physics data
  Reached expected energy resolution of 2.6% for PWO4 modules and 6.2% for lead glass
Obtained preliminary result for HyCal trigger efficiency (>99.5% for E𝛄 > 500 MeV)
Detector alignment accomplished, matching of GEMs and HyCal achieved
Obtained GEM position resolution (72𝛍m) and preliminary detection efficiency (~92%)
Analysis for cross section is ongoing
Cluster Energy E’ vs. Scattering Angle 𝜽
(after cluster matching between GEMs and HyCal, and background subtraction)
1.1 GeV
Preliminary
2.2 GeV
Preliminary

## Slide 15: Summary
The Proton Radius Puzzle is still unsolved after six years
The PRad experiment is a unique piece to the puzzle:
  Lowest Q2 data set (~2x10-4 GeV2) has been collected for the first time in ep elastic scattering experiment
  Data in a large Q2 range (~2x10-4 – 6x10-2 GeV2) have been collected with the same experimental setting
  Large statistics, high quality, rich data has been collected
  Systematic uncertainty well under control by simultaneous measurement of ep elastic and Møller processes
Analysis on the first preliminary result is ongoing
This work was supported in part by NSF-MRI grant PHY-1229153 and US DOE grant DE-FG02-03ER41231