## Slide 3
Each dynode output goes to one of 36
Inputs of the UVA120A Sum module.
Two linear output signals from
UVA120A go to “electronics area”
One of them used for further summation,
The second one was not used in the
PrimEx-1 configuration.
Version #1
Use the second signal (cable) for the timing;
Needs
61 Discriminator channels;
61 channels TDC.

## Slide 5: HyCal and Veto Counters in Hall B Beam Line
Installed in 2004
for PrimEx-I experiment
about 7.5 m from targets
Beam side view
HyCal
He-bag
at 1atm
Veto counters

## Slide 6: PrimEx Hybrid EM Calorimeter (HyCal)
Combination of PbWO4 and Pb-glass detectors (118x118 cm2)
PbWO4 crystals resolution
Pb-glass budget
  34 x 34 matrix of 2.05 x 2.05 x 18 cm3 PbWO4 shower detectors
  (1152 PbWO4 detectors)
  576 Pb-glass shower detectors (3.82x3.82x45.0 cm3)
  2 x 2 PbWO4 modules removed in middle for beam passage
  ≈7.5 m from target
front view, before Light Monitoring System assembly
Good energy and position resolutions:
  σE / E = 2.6% / √E
  σxy / E = 2.7 mm/ √ E
Good photon detection efficiency (≈100%)
Served in 3 precision experiments!
Single PbWO4 detector

## Slide 7: Electromagnetic Calorimeter (HyCal) (Energy Resolutions)

## Slide 8: Electromagnetic Calorimeter (HyCal) (Coordinate Resolution for PbWO4)

## Slide 9: Electromagnetic Calorimeter (HyCal) (Resolutions in Transition Region)

## Slide 10
HyCal and Veto Counters in Hall B Beam Line
Installed in 2004
for PrimEx-I experiment
about 7.5 m from targets

## Slide 11
Energy resolution
Position resolution
Good photon detection efficiency
@ 0.1 – 5 GeV;
Large geometrical acceptance
HyCal
only
HyCal with kinematical
constraint

## Slide 12: HyCal Upgrade (full PbWO4 crystals)
Existing inner part:
34 x 34 =1156 PbWO4 crystal modules
Size: 68 x 68 cm2 area
New PbWO4 modules needed:
~ 576 x 4 = 2,304 PbWO4 modules
Total estimated cost: $3.4 M
Item | quantity | Cost/unit ($) | Cost for item ($)
PbWO4crystals | 2310 | $1000. | 2,310,000
PMT (R1425) | 2310 | $300. | 693,000
HVD | 2310 | $100. | 231,000
Assembly materials | 2310 | $50. | 115,500
TOTAL |  |  | 3,349,500

## Slide 13: PbWO4 Module Development
HVD
G10 PMT housing
with R4125HA tube
VM-2000 and Tedlar
wrapping (38.1 micrometer)
25 micrometer brass strips
Readout cable

## Slide 14: HyCal Temperature Stabilization
Gain vs. temperature: ~ 2% per degrees @ 18 degrees

## Slide 15: Beam Tests: PbWO4 Energy Resolution
6 x 6 crystals
E/E = 1.3 %
1 x 1
3 x 3
HYCAL Beam Test
Prototype Tests

## Slide 16: Beam Tests: PbWO4 Position Resolution
x = 1.3 mm
Prototype Tests
HYCAL Beam Test

## Slide 17: HYCAL: Transition Region

## Slide 18: PbWO4 Detector Response vs. Dose Rate