## Slide 1: Jlab Visit 7/26/2021 J. Mammosser, R. Afanador
- Delivery of couplers
- Discussion and review of string processes and procedures
- Return of the SNS cold compressor
- Discuss RF coupler bias resistor
- Thermal shield weld samples

## Slide 2: Review of string processes and procedures
During our stay we were able to see the following processes:
Disassembly procedure for PPU08, removal of flange bolts
Removal of PPU08 RF coupler and flanges from cavity
HPR of PPU09 in preparation for string assembly
Transfer of PPU11 from rack outside cleanroom and chemroom entry followed by cleanroom entry
Discussed the Ultrasonic cleaning steps
Inspected the flanges on PPU08 after entry into cleanroom

## Slide 3: Observations:
You have the best facilities of any Lab I have visited, maybe best in the world
Chemroom and cleanroom staff are careful to follow procedures closely, we did not see anything that should not produce excellent results
In some cases, the procedures are dynamically changing to address issues
Staff is closely following the scheduled activities which changes frequently

## Slide 4: Observations continued:
Helium vessel is very dirty after welding:
  Tape and residue on surfaces which has to be found and removed
  Surfaces are rough in places where the grinder was used on vessels. These areas hold contamination and are very difficult to clean
  After careful inspection of outside surface penetrations, mounting bolts, , bellows to head gap with portable microscope only a few particles were found, my impression is it was very clean
  On string 2, I was showing Chris how rough the surfaces were and removed a metal flake from one of the areas ground on the shell
With the large number of projects currently running
  Staff are moving back and forth between projects daily
The staff care about each project this is very evident