## Slide 1
THU2 Cosmic test with SDU PMT （3）
Chendi Shen
2018.2.1

## Slide 2
1100V (total number of events: 50)
Npe=622

## Slide 3
1050V (total number of events: 550) npe=680

## Slide 4
HV=1000 V
number of events 870
Npe=657

## Slide 5
HV=900 V
number of events 1330
Npe=711

## Slide 6
Raw Data
HV=800 V
number of events 1160
Raw Data
HV=700 V
number of events 590
Npe = [(Raw data – ped) * 0.1pc/chanel * 10-12 * 9.4] / (Gain * e)
The first peak (49.3/49.4) has nothing to do with high pressure,
So the problem is that long time testing can cause ped to shake.
49.3
49.4
109
70.5

## Slide 7
HV=800 V
number of events 1160
Npe=669
For this long time (70 days) test, DAQ generated shaking, which led to the appearance of the first peak.
Npe=840-171=669

## Slide 8
 | THU PMT |  | SDU PMT
HV | hamamatsu | IHEP | SDU
800 |  |  | 0.527*106
900 | 1.3*106 |  | 1.295*106
1000 | 3.1*106 | 2.2*106 | 2.9*106
1050 |  |  | 4.11*106
1100 | 6.5*106 | 4.5*106 | 5.997*106
1200 | 13.3*106 |  | 11.227*106
1300 | 26.1*106 |  | 
Gain of PMT

## Slide 9
Test results
Chart: Number of photo electron with different Gain
| 800 | 900 | 1000 | 1050 | 1100 | 1200 | 1300 | 1400
hamamatsu（THU PMT） | 750 | 748 | 432 | 271 | 164 | 96
IHEP (THU PMT) | 1054 | 624
SDU (SDU PMT) | 669 | 711 | 657 | 680 | 622
SDU PMT is stable and the result is more reasonable, so Npe of THU2 is around 680.