## Slide 1
fiber reflectivity test
Chendi Shen
2018.6.7

## Slide 2
Lead without powderpainting
MPD_Scintillator
6 layers
Test setup
16 WLSF
BCF91A
PMT
r source
HV
multimeter
Silver shine 415001
r source
Test box
Test box

## Slide 3
Test box

## Slide 4
Test result
 | BCF91A Voltage (mV)
No mirror painting | 640
Silver 415001 | 890
improvement | 39%
 | BCF91A Npe | Y11 Npe
No mirror painting | 24 | 25
Silver 415001 | 34 | 33
improvement | 41.67% | 32%
BCF91A
Y11
Previous test results
03/16/2017 Weekly meeting

## Slide 5
Next to do
Different scintillator
PMT
β
β
Different reflective materials on the end of the fibers.
Different reflective materials between lead and scintillator
Lead
Reflective materials
scintillator
β
scintillator
Scintillator
16 WLSF
Silver shine or TiO2
β
β