## Slide 1
The TRIUMF ARIEL rf modulated electron source
EIC14, March 17-21,
Jefferson Lab, Newport News, VA, USA
F. Ames,
Y. Chao, K. Fong, S. Kocielniak, N. Khan, A. Laxdal, L. Merminga,
C. Sinclaire, D. Storey

## Slide 2: TRIUMF ARIEL
500MeV Cyclotron
ISAC-I
ISAC-II
e-Linac
ARIEL
500 MeV H- cyclotron
up to 400 µA into 4 beam lines,
meson and isotope production
ISAC: SOL facility for the production and acceleration of rare isotope beams (RIB)
Highest power driver beam (50 kW protons)
plus post-accelerator
Now adding ARIEL to increase from one to three simultaneous beams
Add e-Linac (50MeV 10mA cw - 1.3GHz SC linac) to produce rare isotopes via photofission
40MV SC Linac

## Slide 3: e-linac
e-gun(300keV)
ACM2(50MeV)
300 kV supply
ICM(10MeV)
ACM1(30MeV)
klystrons
5 9-cell superconducting
cavities
2K, 1.3 GHz
final energy 50 MeV
continuous beam 10 mA
injection at 300 keV
modulated at 650 MHz
Phase 1 (Sept. 2014)
ICM +ACM1 with 1 cavity
25 MeV

## Slide 4: electron source specifications
rf modulation frequency 650 Mhz,
pulse length +/- 16º (137 ps).
average current 10 mA
charge / bunch 15.4 pC
kinetic energy 300 keV
normalized transverse emittance ~5 µm
duty factor for macro pulsing 0.1-100% (3 W-3 kW)
→ Gridded thermionic source

## Slide 5: rf modulation concept
≈
=
cathode
anode
grid
Ua
Ub+Urf
I(t) = g21 (Ub+Urfcos(ωt) -Uc)
g21: transconductance
Uc: cut off voltage
Triode was used for FELIX @ NIKHEF
R.J. Bakker et al., NIM A307 (1991) 543

## Slide 6
example
g21 = 0.022 Ω-1
Uc = -10 V
ψ = ± 16 º
Q = 15.4 pC
Ub = -201 V
Urf = 198.5 V
Ipeak =165 mA

## Slide 7: 100 kV prototype
place for
emittance meter
Faraday cup
beam stop
cathode
anode
10 cm
collimator
Ø 15 mm
source body
and electrodes on loan
from Jefferson Lab
gridded cathode:
CPI Y-845
First test diagnostics
Faraday cup
Allison type
emittance scanner

## Slide 8: rf matching
impedance at cathode grid ≈ 2 kΩ
rf transformer as dc break between ground and high voltage

## Slide 9: 100 kV prototype measurements
low energy beam line for source testing
macro pulsing to reduce total beam power by modulating rf
SOL1
VS1B
SOL2
SOL3
VS3
SOL1
VS1
MB0
VS1A
rf defl
Image of cathode grid
rf buncher
emit
FC
FC
source

## Slide 10: transversal emittance
10
Fit Point
Measured Point
VLBT
SOL1
X Emittance (m-rad) | 9.28883×10-6
Y Emittance (m-rad) | 9.47943×10-6
scan solenoide

## Slide 11: transversal emittance
Allison Emittance
scanner
Measurement
As function of
solenoid field
Laxdal et al.
BIW’12

## Slide 12: longitudinal emittance

## Slide 13: 300 kV source design
cathode
anode
ceramic insulator
titanium cathode electrodes
copper beryllium anode
reduced surface at
negative potential
steerer magnets

## Slide 14: 300 kV source design
rf tuner
ceramic waveguide
high voltage shroud
support
high voltage feedthrough
SF6 vessel

## Slide 15: ceramic rf waveguide
problem:
rf power is needed on high voltage
generator / amplifier on high voltage | generator / amplifier on ground
easy matching | easy operation and maintenance
high volume and power on high voltage | high voltage dc break for rf not commercially available
operating electronics in SF6 | higher rf losses in transport
first tests with rf transformer: not enough isolation or too high losses

## Slide 16: ceramic rf waveguide
HFSS simulation
Al2O3 ceramic Ø 10 cm

## Slide 17
titanium
Pierce electrode
copper beryllium
anode in ceramic
preparing for leak check

## Slide 18: 300 kV source installation
ceramic waveguide
350 kV, 16 mA
power supply
SF6 vessel inside
SF6 vessel outside

## Slide 19: 300 kV source results
Frist test with ceramic waveguide and 300 kV
Duty factor 0.1% (1 µs, 1 kHz)
Peak current 2-10 mA

## Slide 20: results
Duty factor =1%
average current = 100 μA
pulse current 10 mA
Power = 30 W
εrms,norm=7.5 μm

## Slide 21: longitudinal emittance
Preliminary longitudinal parameters
100% momentum spread:
100% bunch length at gun:

## Slide 22: summary
A 300 kV electron source has been installed for the ARIEL project at TRIUMF
Rf modulation of the gridded thermionic source has been demonstrated
A ceramic waveguide for the transportation of rf power has been used
Average current of the source is up to 10 mA
Macro pulsing (100Hz-10kHz) allows a duty factor of 0.1-100%
Outlook:
Injection into first accelerator cavity (10MeV) May 2014
Acknowledgement:
Many thanks to the electron source group of Jefferson laboratory
for providing us with the 100 kV prototype source body.